## Slide 1: Arduino Workshop #11
Hardware and Timer Interrupts

## Slide 2: Interrupts
An Interrupt's job is to make sure that the processor responds quickly to important events. When a certain signal is detected, an Interrupt (as the name suggests) interrupts whatever the processor is doing, and executes some code designed to react to whatever external stimulus is being fed to the Arduino.

## Slide 3: Hardware Interrupts

## Slide 4: Hardware

## Slide 5: Interrupt Pins on Arduino UNO
The Uno only has two pins that can act as interrupts.
Pin2 = Interrupt 0
Pin3 = Interrupt 1
The Arduino MEGA has 6 interrupts

## Slide 6: Debounce
Buttons and switches are not perfect.
When Pressed, they “Bounce” the voltage before setting on their pressed voltage.
We will use the 74HC14 Hex Inverting Schmitt trigger IC to ensure the button works correctly.

## Slide 7: Button Debounce with
Input of inverter is tied to VCC. When button is pressed, the capacitor discharges slowly through resistor.
When pin 1 is at a critical voltage the inverter output will go high.
Button release is opposite.

## Slide 8: The Circuit

## Slide 9: The Code
Download from UTA EE GitHub
hw_multitask.ino is the file name
Let’s take a quick look at what the code is doing

## Slide 10: Timer Interrupts
The Crystal Oscillator (XOSC) on the Arduino runs at 16MHz.
Timer1 is a 16 bit timer, meaning that it can count up to 216-1, or 65,535.
Once Timer1 reaches 65,535 it resets to 0 and starts all over again.

## Slide 11: The Code
Download the TimerOne-master.zip file and put it in the Arduino libraries folder.
Sketch-> Include Library -> Add ZIP Library Then select the TimerOne-master.zip file.
Download the Timer1.ino file and upload it.
Let’s look at the code

## Slide 12: Sound Machine

## Slide 13: Visual Proof
Measure the input ( Pin1 of the 74HC14) on Channel 1 of the oscilloscope
Measure the output (Pin 2 of the 74HC14) on Channel 2 of the oscilloscope.
Adjust the oscilloscope until you see your button presses on both channels.
Save the picture and/or data to your USB drive if you would like.